## Slide 1: ALL-DIGITAL PLL (ADPLL)
Alicia Klinefelter
ECE 7332
Spring 2011

## Slide 2: Outline
Project Description
  Problem
  Expected Outcomes
  My Approach
Basic Topology of All Digital PLLs (ADPLL)
  Components
  My architecture
Initial Designs and Research
Final Design
  Novelty
    Low power and synthesizeable
Results
Further Work and Conclusions

## Slide 3: PROJECT: ADPLL
Originally only planned to complete DCO.
In order to reduce number of lock cycles, pre-DCO logic needed.
Application space: Sub-threshold ADPLL Clock synthesizer for wireless sensor networks that takes a 50kHz reference and outputs a clock at 500kHz.
Phase noise and jitter constraints are not rigid
  Assuming clock is controlling digital logic
  Amount of jitter in this application will seem large compared to RF
  Main goal is low power and using sleep mode after lock

## Slide 4: PROJECT: ADPLL expectations
Power consumption: < 10uW
Supply Voltage: 400mV (Vt = 410mV for NMOS_VTG)
Phase Noise: < 60dBc/Hz @ 1MHz
Lock cycles: < 10
LSB Resolution: < 1ns
Only gates used (no capacitors, inductors, etc.)
  Some ADPLLs assume only intermediate signals are digital.
  To attempt to make it synthesizeable

## Slide 5: Why are ADPLLs useful?
Problems with analog implementation
  Design and verification
  Settling time
    20 – 30 ms in CPPLLs
    10 ms in the ADPLL
  Implementation cost
    Custom blocks
  Loop Filter
    High Leakage current
    Large capacitor (2) area
  Charge Pump
    Low output resistance
    Mismatch between charging current and discharging current
      Phase offset and reference spurs

## Slide 6: Outline
Project Description
  Problem
  Expected Outcomes
  My Approach
Basic Topology of All Digital PLLs (ADPLL)
  Components
  My architecture
Initial Designs and Research
Final Design
  Novelty
    Low power and synthesizeable
Results
Further Work and Conclusions

## Slide 7: All-digital PLL (ADPLL) TOPOLOGY
Time-to-Digital
Converter (TDC)
Digital Loop Filter
Divider
ref(t)
DCO
out(t)
Why the loop filter?

## Slide 8: Outline
Project Description
  Problem
  Expected Outcomes
  My Approach
Basic Topology of All Digital PLLs (ADPLL)
  Components
  My architecture
Initial Designs and Research
Final Design
  Novelty
    Low power and synthesizeable
Results
Further Work and Conclusions

## Slide 9: ADPLL: Time-to-digital converter I
Architectures
Delay chain structure sets resolution
Mismatch causes linearity issues
Resolution: want low quantization noise
Time-to-Digital
Converter (TDC)
Digital Logic Controller
Divider
ref(t)
DCO
out(t)
div(t)
[1, Perrott]
Notes: Perrott mentions these are a very promising research area!

## Slide 10: ADPLL: Time-to-digital converter II
Perrott presented a ring-oscillator based TDC
  Counts number of pulses between the two rising edges of the clock
  Determines which is leading /lagging
  Output goes to digital logic block to control DCO
Large range with compact area
Difficult to find in literature used for ADPLL
Why would a filter be needed?
[1, Perrott]
Notes: Perrott mentions these are a very promising research area!

## Slide 11: ADPLL: Time-to-digital converter II
Final schematic of the TDC.
1.43μW @ 0.4V
9-bit up-counter
registers<8:0>
oscillator
reset logic
leading/lagging logic
Notes: Perrott mentions these are a very promising research area!

## Slide 12: ADPLL: Time-to-digital converter II
Notes: Perrott mentions these are a very promising research area!

## Slide 13: ADPLL: DCO
Time-to-Digital
Converter (TDC)
Digital Loop Filter
Divider
ref(t)
DCO
out(t)
Replaces the VCO from analog implementations
Consumes 50-70% of overall ADPLL power
Generally consists of a digital controller implementing frequency acquisition algorithm and oscillator.

## Slide 14: DCO: DELAY CELLS
Many options
  Standard inverter
  Hysteresis Delay
  Current Starved
  Shunt Capacitor
Most low power applications for ADPLLs use inverters or hysteresis delay cells (for fine stage).
  LSB resolution doesn’t need to be incredibly small for our application.

## Slide 15: DCO: DELAY CELLS
The four different delay cells that were investigated.
Shunt Capacitor
Inverter
Hysteresis Delay
Current Starved

## Slide 16: Delay cells: frequency

## Slide 17: Delay cells: POWER

## Slide 18: DCO: ARCHITECTURE

## Slide 19: DCO: SCHEMATIC
Linear Range: 430kHz-680kHz
Power (all on):
935.2nW
Fine tuning
Coarse tuning
output
feedback

## Slide 20: DCO: COARSE STAGE rANGE

## Slide 21: DCO: FINE STAGE RANGE
LSB Resolution: 692ps

## Slide 22: DCO: Example output
Coarse Code:
0010_0000_0000
Fine Code:
0000_0000_0000
0000_0000_0000
1000_0000_0000
0000_0000
Output Frequency:
650.2kHz

## Slide 23: Outline
Project Description
  Problem
  Expected Outcomes
  My Approach
Basic Topology of All Digital PLLs (ADPLL)
  Components
  My architecture
Initial Designs and Research
Final Design
  Novelty
    Low power and synthesizeable
Results
Further Work and Conclusions

## Slide 24: DESIGN COMPARISONS: POWER
Power | Op. Freq | Voltage
5.4uW | 3.4MGHz | 1 V
5.2uw | 3.89MHz | 1 V
8mW | 12.3MHz | 1.2 V
1.7mW | 20MHz | 1 V
166uW | 163.2MHz | 1 V
140uW | 200MHz | 1 V
110uW | 200mhZ | 0.8 V
75.9uW | 239.2MHz | 1 V
340uW | 450MHz | 1.8 V
1.7mW | 560MHz | 1.2 V
2.3mW | 800MHz | 0.9 V
23.3mW | 1GHz | 1.8 V
5.5mW | 5.6GHz | 0.7 V
1uW | 650kHz | 0.4V

## Slide 25: DESIGN COMPARISONS: TUNING RANGE

## Slide 26: ADPLL: LOGIC BLOCK
Takes number of pulses counted from TDC, determines the number of coarse and fine delay stages needed.
Uses one-hot encoding for the outputs of the transmission gates.
Once coarse/fine stages are known, uses headers to turn off delay cells not being used
Improvement on binary search
  Uses initial number of pulses to determine where to start search
  Number of pulses used to determine how many steps to take during next search step
Notes: Perrott mentions these are a very promising research area!

## Slide 27: Future work
Synthesize Logic
  Use familiar technology with standard cells
  Replace with my own library cells created in FREEPDK
Do final system simulation
  Frequency divider not mentioned here, nothing new
  It consumes 6.6nW at 400mV
Corner, Temperature simulations
Notes: Perrott mentions these are a very promising research area!

## Slide 28: RESOURCES
All papers in the bibliography section of Wiki were used for plot generation and comparisons of DCOs
CPPSIM Tutorials
  [1, Perrot] PLL  Digital Frequency Synthesizers